HOME COMPOSTING

WITHOUT ATTRACTING RODENTS

When a homeowner chooses to compost fruit and vegetable scraps with their yard trimmings, a rodent resistant bin is the best choice. Rodent resistant bins require a lid, a floor, and no opening greater than ¼”. There are many different ways to compost, and  several good choices that eliminate any possible rodent issues;  some of these are  displayed at the composting demonstration site.

PROPER HANDLING OF FOOD SCRAPS

Food scraps must be buried in any compost pile, but if rodents are a problem, then food scraps should be added only in closed bin systems. No meat or dairy products should ever be added to a home compost pile, and eliminating bread and other types of grains from the compost pile will also reduce the attraction. Homeowners can also hang strips of cloth soaked in ammonia around their compost area as a strong deterrent against scavengers.

CLOSED BINS

Bins such as the Smith and Hawken  ‘ Bio-Stack ‘ or  the ‘ Garden Gourmet ‘ are designed with a lid. The bin can be set on a gravel pad, or a ¼ “ wire mesh bottom to prevent animals digging in.  If  rodents are already numerous and problematic in a given area; then the existing ½ “  ventilation slits in these bins may need to be screened as well.

COMPOST TUMBLERS

These compost systems are completely rodent proof since they are completely enclosed, and many of the tumbler designs are also elevated above the ground.

WORM BINS

The Upward-Migration Worm bins are completely enclosed, and elevated on legs. Ventilation holes are too small for rodents to enter, but if the system is outside, weights on the lid are necessary to prevent larger scavengers such as raccoons from entering the bin. These systems can also be set up in a garage.

FOOD DIGESTERS

Cut out the bottom of a plastic garbage can,  punch some holes at the bottom portion of the sides, then sink the can into a 12” deep hole in the ground. Pack the soil in around to secure it; add your compostable materials, and be sure to secure the lid as well.

PIT OR TRENCH COMPOSTING

Dig a 12 – 18” deep trench or post hole in the ground; place your compostable materials into the hole, taking care to cover over new additions with a layer of soil. Fertile planting sites can be prepared in advance using this composting method.

Charlotte Torgovitsky – torgovitsky@comcast.net – 415-892-9148